## Slide 1: 3D Thermal Solver for Chiplet-Based GPU Packages
ECE201A: VLSI Design Automation Final Project
Ethan Owen
Rachel Sarmiento
March 13, 2026
Background
Project
Modern high-performance processors use chiplet-based architectures where multiple dies (GPUs and HBM stacks) are integrated within a single package
Challenges include high power density, 3D heat spreading, stacked memory (HBM), complex package-level cooling
Thermal modeling informs chiplet placement, package design and cooling system
Developed a physics-based thermal solver that models 3D heat conduction in chiplet-based GPU packages, considering material stackups and geometry
Generates thermal RC network and solves with PySpice
Assumptions:
GPU Power = 270W
HBM Stack Power = 5W each
Power_Source = 0W
Ambient = 45C
GPU/HBM heat deposited on center z-plane
Water-cooled top boundary uses HC derived from correlation and capped by XML

## Slide 2: Thermal Solver Block Diagram
Voxel Grid Generation
Material Assignment
Power Mapping
Thermal RC Network
PySpice Solver
Temperature Extraction
Results Extraction
Parse chiplet/package geometry from provided XML flow to discretized into a non-uniform adaptive voxel mesh
Each voxel is assigned thermal properties based on its material and stackup
Conductivity is considered separate for in-plane and vertical plane
Power is deposited at the center z-plane of each die, matching physical location of transistor heat generation
Neighboring voxels are connected by thermal resistances in x, y, and z-directions
Boundary conditions include convection to heatsink and convection at the bottom
Thermal RC network exported to PySpice for solving
Results from PySpice generate the temperatures for each voxel
Compare reference case to our results, calculate variances, generate overall runtimes and values for each config
Output to results file

## Slide 3: Methodology Key Features
  Geometry edges (material boundary, chiplet edge, layer boundary) define the base grid to prevent smearing of materials across voxels
  Max Dimension Rule: Max X, Y = 2mm, Max Z = 0.3mm, selected to increase accuracy
  Min Dimension Rule: prevents excessive run time
  Smart Subdivision Algorithm: Large regions are subdivided into smaller cells based on region span and max dimension rule
  We achieve high resolution near chiplets and low resolution in uniform regions
Non-Uniform Adaptive Voxel/Box Mesh
  Consider conductivity in the X,Y-plane and the Z-plane as separate conductivities
  Use parallel mixing for X,Y-plane and series mixing for Z-plane
Anisotropic Material Modeling
  Primary solver is PySpice
  Backup solvers in case of issues -- SciPy Sparse Solver or Numpy SOR Iteration
SPICE Thermal Simulation with Robust Multi-Backend Solver
  Determines fluid velocity and heatsink dimensions to compute Reynolds Number and Nusselt Number for convection coefficient
Water Cooling Model

## Slide 4: Results Summary
CONFIG: ECTC_2p5D_1GPU_8high_110325_higherHTC
  max temp gpu: 101.260618 C
  max temp hbm: 93.495963 C
  avg temp gpu: 99.092325 C
  avg temp hbm: 91.218611 C
  total time: 95.776 s
  pyspice time: 93.601 s
  placement time: 0.491 s
CONFIG: ECTC_3D_1GPU_8high_120125_higherHTC
  max temp gpu: 122.017986 C
  max temp hbm: 122.340038 C
  avg temp gpu: 121.264252 C
  avg temp hbm: 122.023830 C
  total time: 29.438 s
  pyspice time: 28.329 s
  placement time: 0.012 s
CONFIG: ECTC_3D_1GPU_8high_110325_higherHTC
  max temp gpu: 126.400908 C
  max temp hbm: 125.303826 C
  avg temp gpu: 124.552848 C
  avg temp hbm: 124.813398 C
  total time: 29.415 s
  pyspice time: 28.282 s
  placement time: 0.012 s
  peak variance: 0.683685 C^2
  average variance: 0.652491 C^2
  peak temp vs golden: 0.271364 C
  average temp vs golden: 0.250548 C
  average variance match vs golden: 97.90%
2.5D configuration significantly reduces temperature while 3D stacked design produces higher thermal density
PySpice dominates run time
Comparison to golden reference case shows similar peak and average temperatures

## Slide 5: Conclusion
The developed 3D voxel-based thermal solver converts heat transfer into a thermal RC network solved with PySpice
The non-uniform adaptive voxel grid aligned to package geometry and was broadened for uniform areas, balancing accuracy and computational effort
Physical modeling included anisotropic material conductivities, center-plane power modeling for dies, and physics-based convection estimates for water cooling
Solver applied to case with GPU of 270W, HBM stack of 5W each, and ambient of 45C
Future improvements could include integration with chiplet placement optimization, isolator incorporation, and more detailed cooling models
Overall, solver provides a flexible and scalable framework for thermal analysis of advanced GPU packaging architectures
Results for reference case closely matched with reasonable run time, dominated by PySpice solver